## Slide 1
QUASAR-SNN:
Design and FPGA Implementation of a Quantized, Activity-Aware and Sparse Spiking Neural Network Accelerator for Onboard Remote-Sensing Applications
Dissertation - Progress Review
Submitted by,
Xwin J Thomas
NDU202500365
M.Tech EDT
Guided By,
External Guide: Sravan Mohan, Project Manager, Processor Systems (India) Private Limited
Internal Guide:
NIELIT CALICUT
राष्ट्रीय इलेक्ट्रॉनिकी एवं सूचना प्रौद्योगिकी संस्थान
National Institute of Electronics and Information Technology
Deemed to be University under Distinct Category

## Slide 2
Research Problem
2
Central question
Can the selected hybrid SNN retain its accuracy advantage over early encodings when mapped to a fixed-point, event-driven FPGA datapath?
Current evidence
Model selection and software precision studies are complete. The selected T10 model achieves 92.32% held-out accuracy.
Unresolved claim
Resource, latency and energy benefits remain to be demonstrated on hardware; activity-weighted operation counts alone cannot establish them.
Notes: Source: Progress slides 4, 20, 25
All numerical results are reproduced from the supplied progress-review deck; training logs and checkpoints were not independently inspected. Proposed tests and unresolved questions are not measured results.

## Slide 3
Selected Model Architecture
3
RGB image
3 × 64 × 64
→
Conv1 + BN
computed once
→
Static current
LIF1 + pool
→
Conv2 / Conv3
LIF + pool
→
FC1 spikes
FC2 readout
T = 10 | ~549k parameters | 10 EuroSAT classes
Conv1 contributes 1.77M dense MACs per image; downstream layers contribute 14.70M spike-driven ACs.
Static-current reuse is an architectural opportunity; its storage and access costs still need measurement.
MAC and AC counts are reported separately; they have different implementation costs.
Notes: Source: Progress slides 6, 8, 20
All numerical results are reproduced from the supplied progress-review deck; training logs and checkpoints were not independently inspected. Proposed tests and unresolved questions are not measured results.

## Slide 4
CNN and Hybrid SNN Comparison
4
Earlier T14 study | Accuracy (%) | Macro-F1 (%)
CNN · 3 seeds | 92.95 ± 0.48 | 92.81 ± 0.48
Hybrid SNN · 3 seeds | 92.86 ± 0.41 | 92.74 ± 0.42
Similar scores across three seeds support comparable performance. They do not establish statistical equivalence or an accuracy improvement.
Notes: Source: Progress slides 6, 9
All numerical results are reproduced from the supplied progress-review deck; training logs and checkpoints were not independently inspected. Proposed tests and unresolved questions are not measured results.

## Slide 5
Timestep Selection
5
T | Val. accuracy (%) | Val. macro-F1 (%) | Downstream AC
6 | 92.00 | 91.89 | 9.45M
10 · selected | 92.52 | 92.44 | 14.71M
14 | 93.06 | 92.96 | 22.91M
T10 reduces validation AC by 35.77% versus T14 for a 0.52 percentage-point reduction in macro-F1. Selection used validation data.
Notes: Source: Progress slides 17–19
All numerical results are reproduced from the supplied progress-review deck; training logs and checkpoints were not independently inspected. Proposed tests and unresolved questions are not measured results.

## Slide 6
Held-Out Evaluation: T10
6
Metric | Validation | Test · 4,050 images
Accuracy | 92.52% | 92.32%
Macro-F1 | 92.44% | 92.23%
Downstream AC / image | 14.71M | 14.70M
The test score is close to validation. T10 robustness across seeds and geographically independent evaluation remain unreported.
Notes: Source: Progress slide 20
All numerical results are reproduced from the supplied progress-review deck; training logs and checkpoints were not independently inspected. Proposed tests and unresolved questions are not measured results.

## Slide 7
Quantization Results: Earlier T14 Model
7
Configuration | Test accuracy (%) | Interpretation
FP32 | 92.59 | Reference
Fixed16 | 92.47 | 0.12 pp reduction
Uniform Fixed8 | 44.57 | Severe degradation
I12 / W12 / C12 / M12 | 92.35 | 0.24 pp reduction*
*Computed from the rounded displayed accuracies. This is a T14 result; 12-bit T10 performance after pruning is still unknown.
Notes: Source: Progress slides 10, 14
All numerical results are reproduced from the supplied progress-review deck; training logs and checkpoints were not independently inspected. Proposed tests and unresolved questions are not measured results.

## Slide 8
Why the 8-Bit Model Failed
8
Observed numerical mismatch
mem1 LSB = 2.0 against a threshold of approximately 1.125. mem4 LSB = 8.0, approximately 16× its learned threshold.
Precision localization
Widening membranes alone changed accuracy little when currents stayed at 8 bits. Wider current paths produced the larger recovery.
Implication for RTL
Zero observed saturation does not establish numerical fidelity. Rounding, threshold crossing and state-update order must be matched explicitly.
Notes: Source: Progress slides 11–13; RTL implication is a proposed verification requirement
All numerical results are reproduced from the supplied progress-review deck; training logs and checkpoints were not independently inspected. Proposed tests and unresolved questions are not measured results.

## Slide 9
Activity Profile: Where Work Remains
9
T10 test activation | Spike density | Design question
Pool1 | 21.87% | Early event traffic
Pool2 | 8.48% | Sparse convolution scheduling
Pool3 | 7.04% | Memory access versus idle cycles
FC1 | 46.79% | Dense activity in the classifier
FC1 has the highest reported spike density. Density alone does not identify the largest energy cost; fan-out, state updates and memory traffic also matter.
Notes: Source: Progress slide 20
All numerical results are reproduced from the supplied progress-review deck; training logs and checkpoints were not independently inspected. Proposed tests and unresolved questions are not measured results.

## Slide 10
FC1 Pruning: A Targeted Experiment
10
Why start here
FC1 is 4096 → 128: 524,288 weights, about 95.5% of the reported ~549k parameters. It also has 46.79% spike density.
Proposed screen
Compare 128 / 112 / 96 / 80 / 64 neurons using validation macro-F1, activity and estimated storage. Fine-tune the selected configuration.
Question to resolve
Do fewer FC1 neurons reduce BRAM and cycles after packing and scheduling? Recalibrate T10 precision after pruning before drawing conclusions.
Pruning is prepared, not executed. No post-pruning accuracy or hardware saving is claimed.
Notes: Source: Progress slides 6, 16, 20, 21; FC1 share calculated from supplied dimensions
All numerical results are reproduced from the supplied progress-review deck; training logs and checkpoints were not independently inspected. Proposed tests and unresolved questions are not measured results.

## Slide 11
Hardware Benefits Still Need Measurement
11
Static-current reuse
Conv1 can run once per image, but holding the feature map may increase BRAM occupancy and repeated read traffic.
Event processing
Sparse spikes can avoid synaptic work. Queue management, irregular accesses and neuron-state updates may offset the saving.
12-bit representation
Arithmetic width and physical storage width are different. Actual BRAM packing, DSP mapping and Fmax must determine the benefit.
Notes: Source: Progress slides 8, 22, 25; questions derived from the proposed architecture
All numerical results are reproduced from the supplied progress-review deck; training logs and checkpoints were not independently inspected. Proposed tests and unresolved questions are not measured results.

## Slide 12
Generalization and Evidence Gaps
12
Dataset independence
The supplied slides do not document spatially disjoint splits. Geographic leakage and performance on unseen regions need investigation.
Class-level errors
Macro-F1 is reported, but per-class recall and the confusion matrix are not shown. Identify systematic land-cover confusions before model freeze.
Onboard relevance
EuroSAT RGB classification is a controlled benchmark. Sensor changes, atmospheric effects and radiation reliability remain outside the demonstrated result.
Notes: Source: Progress slides 6, 17, 20; abstract references include reliability literature. These are open questions, not observed defects.
All numerical results are reproduced from the supplied progress-review deck; training logs and checkpoints were not independently inspected. Proposed tests and unresolved questions are not measured results.

## Slide 13
Model Freeze and RTL Verification
13
Stage | Required evidence
Pruned T10 | Validation-based choice; fine-tuning and activity report
Fixed-point reference | Q-formats, rounding, overflow, reset and update order
Layer verification | Currents, membrane states, spikes and class accumulator
Hardware evaluation | Resources, Fmax, cycles, latency and energy / image
Preserve the tested unpruned checkpoint. Freeze the revised model before its final held-out evaluation.
Notes: Source: Progress slides 15, 21, 23, 26; explicit arithmetic semantics are proposed requirements
All numerical results are reproduced from the supplied progress-review deck; training logs and checkpoints were not independently inspected. Proposed tests and unresolved questions are not measured results.

## Slide 14
Decisions for the FPGA Phase
14
Prototype scope
Full-network time-multiplexed inference or a representative event-processing block? Define what the first implementation must demonstrate.
Device and memory budget
Select the FPGA, clock target, on-chip storage budget and external-memory assumptions before choosing processing-element parallelism.
Acceptance criterion
Agree on acceptable accuracy loss and a hardware baseline. Compare dense and event-driven execution under the same measurement conditions.
Notes: Source: Progress slides 24–26; device/budget remain unspecified in the supplied progress evidence
All numerical results are reproduced from the supplied progress-review deck; training logs and checkpoints were not independently inspected. Proposed tests and unresolved questions are not measured results.

## Slide 15
Current Position
15
Established
T10 selected on validation; 92.32% test accuracy and 92.23% macro-F1. Earlier T14 studies support a 12-bit starting point.
Next experiments
Structured FC1 pruning → fine-tuning → T10 quantization → bit-accurate reference → RTL verification.
Remaining contribution
Demonstrate whether reduced activity and precision translate into a measured FPGA resource–latency–energy benefit.
Notes: Source: Progress slides 20, 21, 28
All numerical results are reproduced from the supplied progress-review deck; training logs and checkpoints were not independently inspected. Proposed tests and unresolved questions are not measured results.

## Slide 16
Selected References
16
[1] N. Abderrahmane et al., “SPLEAT: SPiking Low-power Event-based ArchiTecture for in-orbit processing of satellite imagery,” IJCNN, 2022. DOI: 10.1109/IJCNN55064.2022.9892277.
[2] D. Padovano et al., “SpikeExplorer: Hardware-Oriented Design Space Exploration for Spiking Neural Networks on FPGA,” Electronics, 2024. DOI: 10.3390/electronics13091744.
[3] R. Pitonak et al., “CloudSatNet-1: FPGA-Based Hardware-Accelerated Quantized CNN for Satellite On-Board Cloud Coverage Classification,” Remote Sens., 2022. DOI: 10.3390/rs14133180.
[4] P. Rech, “Artificial Neural Networks for Space and Safety-Critical Applications: Reliability Issues and Potential Solutions,” IEEE Trans. Nucl. Sci., 71(4), 377–404, 2024.
Notes: Source: References reproduced from the supplied abstract-review deck; bibliographic entries have not been independently verified.
All numerical results are reproduced from the supplied progress-review deck; training logs and checkpoints were not independently inspected. Proposed tests and unresolved questions are not measured results.

## Slide 17
Discussion
17
What should the first FPGA prototype prove?
• Functional equivalence to the fixed-point model
• A measurable benefit from event-driven execution
• A realistic memory and timing budget
Xwin J Thomas | M.Tech EDT | NIELIT Calicut
Notes: Source: Progress slide 26
All numerical results are reproduced from the supplied progress-review deck; training logs and checkpoints were not independently inspected. Proposed tests and unresolved questions are not measured results.